## Slide 1: The rescue company 1

## Slide 2: HELICOPTER SHORT-HAUL part 2

## Slide 3: Rescuer Head-to-toe Safety Checklist (HEC Techniques)
Helmet - properly fitted, chin strap fastened.
Eye protection - secured.
Fire resistant clothing -collar up, flight suit zipped, and loose items around neck tucked in.

## Slide 4: Rescuer Head-to-toe Safety Checklist (HEC Techniques)
Radio - operational and correct frequency selected.
Gloves - on.

## Slide 5: Rescuer Head-to-toe Safety Checklist (HEC Techniques)
Sleeves - down and secured over gloves.
Harness - properly fitted, buckles correctly fastened, no twists, and loose straps secured. Double-check follow-through buckles. Means of attachment is properly secured to harness and locking carabiners are functional.

## Slide 6: Rescuer Head-to-toe Safety Checklist (HEC Techniques)
Knife - easily accessible and secured.
Footwear -Aviation Life Support Equipment (ALSE) approved
Top of boots covered -pants or flight suit provides coverage in seated position, if riding in aircraft.

## Slide 7: Helicopter Short-Haul Checklist (Pre-Mission)
Cargo - non essential items removed. Additional equipment secured.
Cabin - configured for short-haul mission (e.g. doors removed, etc.)
Anchor- anchor points and release system installed, tested, and secure.

## Slide 8: Helicopter Short-Haul Checklist (Pre-Mission)
Short-haul line - correctly attached to primary and backup anchors.
Spotter attachment - tether secure.
Seat belts - secured and operational.

## Slide 9: Helicopter Short-Haul Checklist (Pre-Mission)
Radios - operational (radio check performed) and correct frequency selected.
Intercom - operational. (Use of a "hot microphone" is not advisable, due to other air traffic or ground personnel attempting to make radio contact).

## Slide 10: QUALIFICATIONS AND REQUIREMENTS

## Slide 11: PILOT REQUIREMENTS
A safe and effective short-haul program is highly dependent upon precision longline skills. Accordingly, pilots must comply with the following minimum requirements:

## Slide 12: PILOT REQUIREMENTS
Qualified in accordance with 14 CFR 133 for Class A and B external load operations and meet pilot requirements identified in the procurement document.
50 hours Pilot-In-Command (PIC) in make and model in the preceding 12 months.

## Slide 13: PILOT REQUIREMENTS
25 hours of vertical reference experience requiring precision placement in the preceding 12 months.

## Slide 14: PILOT REQUIREMENTS
Approved for longline operations.
Pass the OAS-administered Short-Haul Pilot Practical Test outlined in the lnteragency Helicopter Practical Test Standards (PTS).

## Slide 15: PILOT REQUIREMENTS
Complete annual operational training with the using unit.
Understand short-haul techniques, short-haul/spotter signals and operational concerns.

## Slide 16: PILOT REQUIREMENTS
Demonstrate ability to work with the short-haul spotter(s).

## Slide 17: SPOTTER AND SHORT-HAULER REQUIREMENTS
Spotters and short-haulers must complete the following minimum requirements. Additional training may be required of an individual based on the complexity of the program.

## Slide 18: Check Spotter
Have demonstrated ability as an instructor and assisted in the training of at least two Spotters.

## Slide 19: Check Spotter
Have completed the Interagency Helicopter Crewmember course.
Be familiar with the helicopter procurement documents.

## Slide 20: Under the supervision of a qualified check spotter:
Demonstrate knowledge of the inspection, care and maintenance of short-haul equipment.
Demonstrate ability to rig the helicopter for short-haul, to provide a safety briefing and to conduct a safety check of short-haul personnel without procedural error.

## Slide 21: Under the supervision of a qualified check spotter:
Demonstrate knowledge of emergency procedures.
Spot six loads of short-haul personnel, two in typical terrain. If applicable, spot four loads of cargo (e.g., a rescue litter) without procedural error.

## Slide 22: Under the supervision of a qualified check spotter:
Demonstrate ability to work with the pilot.
Demonstrate knowledge of risk assessment and mission structure.

## Slide 23: Short-Hauler
Have completed the lnteragency Helicopter Crewmember Training course .
Demonstrate knowledge of the inspection, care and maintenance of short-haul equipment and rigging.

## Slide 24: Short-Hauler
Demonstrate knowledge of short-haul procedures.
Demonstrate knowledge of emergency procedures.

## Slide 25: Short-Hauler
Complete a minimum of four short-hauls, two in typical terrain, without procedural error.
Demonstrate knowledge of mission components and ability to perform risk assessments.

## Slide 26: PROFICIENCY REQUIREMENTS

## Slide 27: Pilot Proficiency
Precision longline, which may include HEC every 30 days. HEC mission every 90 days.

## Slide 28: Pilot Annual Refresher
Meet Operational training. Demonstrate ability to short-haul.

## Slide 29: Check spotter Proficiency
Operational training. Spot four loads without procedural error.

## Slide 30: Short-Hauler Proficiency
Operational training. Complete two short-hauls, one of which must be in typical terrain, without procedural error.